## Slide 1: Mavlink
Kenyatta University, 17.01.2025

## Slide 2: Communicating with your UAV

## Slide 3: MAVLink
Open-source messaging protocol for drones
Use for telemetry and command
Communication with ground control stations such as Mission Planner
Wired or wireless connections
Talk mavlink in Python using Pymavlink
Pymavlink
  Request and set parameters
  Receive state information
  Send servo control commands
  Arm/disarm, change flight mode
  Set waypoints
  Everything you can do with MP
mavlink
mavlink
mavlink
mavlink
mavlink
mavlink
mavlink
mavlink
mavlink

## Slide 4: Mavlink Ressources
PyMavlink examples and documentation
  ArduSub book! ardusub.com/developers/pymavlink.html
Mavlink Documentation
  https://mavlink.io/en/messages/common.html
Today’s presentation and scripts
  https://github.com/meierkilian/ArdupilotIntro

## Slide 5: Practicals

## Slide 6: Download today’s scripts
  https://github.com/meierkilian/ArdupilotIntro

## Slide 7: Installing python
Installing python
  Download Python from: www.python.org/downloads/
  Add python.exe to PATH
  Run and click “Install now”
Installing Pymavlink
  Open terminal (WIN+R, then type “cmd” and press Enter)
  Run “pip install pymavlink”
  Run “pip install requests”
Hello world script
  Create a script “helloworld.py”
  Run “python helloworld.py”

## Slide 8: Start SITL

## Slide 9: Task 1: connection and heartbeat
Start SITL
  Create a quad copter
  Ctrl + F, Mavlink, TCP Host, Write access, Connect
Connection
  Depends on the scenario
  connection = mavutil.mavlink_connection(‘tcp:127.0.0.1:14550’)
Heartbeat
  message = connection.recv_match(type='HEARTBEAT', blocking=True).to_dict()
  Waits for a message of type HEARTBEAT

## Slide 10: Task 2: get telemetry (or any message)
Have a look at common mavlink message and find a message that will give you the global position of the drone.
  https://mavlink.io/en/messages/common.html

## Slide 11: Task 3: taking-off
Taking-off includes three steps
  Change the aircraft to the GUIDED mode
  ARM the aircraft
  Take-off
So three commands have to be sent!

## Slide 12: Task 3: taking-off: mode change

## Slide 13: Task 3: taking-off: arming
Command name: MAV_CMD_COMPONENT_ARM_DISARM

## Slide 14: Task 3: taking-off: take-off
Command name: MAV_CMD_NAV_TAKEOFF

## Slide 15: Task 4: send a waypoint command

## Slide 16: Task 5: send a WP to remote SITL
Connect to local network
  SSID: ANVLAN729
  Password: ministrylevel369
Change connection to your groupe IP
Change the “target system” to your group ID