## Slide 1: Rhino search challenge
Kenyatta University, 21.01.2025

## Slide 2: Background
Ol Pejeta is home to the last two remaining northern white rhinos, and a sanctuary for over 165 critically endangered black rhinos.
The black rhinos need to be seen every 3 days.
If that’s not the case, search parties are sent out in the parc until they find the missing rhino.
Drones might be able to help this effort!

## Slide 3: Rhino search challenge
Each team gets to control a drone in Ol Pejeta
The drone is equipped with a rhino range sensor and a downward-facing camera
  The range sensor has a detection range of 200m.
  The camera has a field of view of 50m on the ground.
Your goal is to find a strategy to find and take a picture of all the rhinos in the park.

## Slide 4: Practicals
Remote simulated drones
Try different search strategies
Software with holes to fill

## Slide 5: Download today’s scripts
  https://github.com/meierkilian/ArdupilotIntro
  Extract it!

## Slide 6: Installing python packages
Packages
  Open terminal (WIN+R, then type “cmd” and press Enter)
  pip install numpy
  pip install dronekit
  pip install pymap3d
Run helloworld.py
  Change directory to the folder “Practicals/RhinoChallenge”
  python helloworld.py
Open “rhinoChallengeTasks.py” in your favourit text/code editor

## Slide 7: TASK 1: is a waypoint reached?
How can we check if a waypoint is reached?

## Slide 8: TASK 2: wait until a waypoint reached?
How can we send a drone to a waypoint and then wait until it reached it?

## Slide 9: TASK 3: Connect to the drone
Connect to local network
  SSID: ANVLAN729
  Password: ministrylevel369
Fill in the system ID of your group
  See the screen for your group IP address and port

## Slide 10: TASK 4: run the manual search
Can you find any rhino?
Is it a convenient way of searching?

## Slide 11: TASK 4: run the manual search
Can you find any rhino?
Is it a convenient way of searching?

## Slide 12: TASK 5: Search Patterns
Lawnmower
Spiral

## Slide 13: TASK 5: lawnmower pattern
Explain what those 4 lines do.
  What are pNW, pNE and PSW?
  Why divided by sensorRange?
  What about 2**0.5?
  Why +1?
  What does the linspace() function do?
pNW
pNE
pSW

## Slide 14: TASK 6: run the lawnmower search
Can you find any rhino?
Is it more efficient than manual search?
What is the drawback of this search?

## Slide 15: TASK 7: triangulation
How should we use the range finder?

## Slide 16: TASK 7: triangulation
How should we use the range finder?

## Slide 17: TASK 7: triangulation
How should we use the range finder?

## Slide 18: TASK 8: run the triangulation search
Can you find any rhino?
Is it more efficient than the lawnmower search?
Do you think a rhino ranger finder is something we can build?

## Slide 19: Conclusion
Give an overview of how to design and conduct a safe semi-autonomous drone (quadcopter) operation in the context of wildlife conservation.
  Autopilot software and simulation (Ardupilot)
  Ground Control Station software (Mission planner)
  Communication protocol (Mavlink)
  Safe operation (SORA)
  Practical work

## Slide 20: Accessing the sensor
Send a sense request to the sensor.
Returns
  {"state": "out_of_range", "distance": -1}
  {"state": "found", "distance": <dist>}
  {"state": "in_range", "distance": <dist>}
Sensor characteristics
  The range sensor has a detection range of 200m.
  The camera has a field of view of 50m on the ground.